Mathematical treatise: Fixed time-step issue
Angular collision response have a dynamic contact time depending on distance to the torque axis.

alignl stack { ΔH : "Change in angular momentum." # vec r : "Offset to point of contact." # J_vec r : "Particle momentum." # vec w "&" vec w_{vec r}: "Angular velocity." # Δs : "Collision contact stretch, relative to" M_ΔH "." # Δt_f : "Fixed time periodicy of simulation." # Δt_d(vec r) : "Real contact duration time." # c_Δt = Δt_d / Δt_f : "Regulating time coefficient." }
# Objective
Present a formula for the c_Δt coefficient, that can be implemented into a 3D physics engine with fixed time periodicy.
# Calculus
alignl c_Δt ~=~ { alignc {Δt_d( vec r )} over Δt_f } `,~~ Δt_f "is a constant."
alignl stack { abs vec w_{vec r} ~=~ abs left ( alignc matrix { H_x^, {(r_y^,)^2 + (r_z^,)^2} over I_Sxx , # H_y^, {(r_x^,)^2 + (r_z^,)^2} over I_Syy , # H_z^, {(r_x^,)^2 + (r_y^,)^2} over I_Szz } right ) # abs vec w ~=~ abs left ( alignc matrix { H_x^, 6 over I_Sxx , # H_y^, 6 over I_Syy , # H_z^, 6 over I_Szz } right ) } [1]
[1] Converting angular momentum [kg*m^2/s] to angular velocity [radians/s] by Dan Andersson
left lbrace alignl stack { Δs ~=~ Δt_d( vec r ) * abs vec Δw_{vec r} # Δs ~=~ Δt_f * abs vec Δw } right rbrace ~rightarrow~ Δt_d( vec r ) * abs vec Δw_{vec r} ~=~ Δt_f * abs vec Δw ~rightarrow~ {alignc {Δt_d( vec r )} over Δt_f } ~=~ {alignc abs vec Δw over abs vec Δw_{vec r}} ~=~ c_Δt

alignl c_Δt ~=~ {alignc abs vec Δw over abs vec Δw_{vec r} }
alignl vec r ", " vec Δw " and " vec ΔH is known and alignl vec Δw_{vec r} can be derived from those three.
# Pseudo Code
if ( |vecR| > 1 ) vecDeltaH * = AngularImpactTimeCoefficient( vecR, vecDeltaW, vecDeltaH );
# Optimization
alignl c_Δt ~=~ {alignc abs vec Δw / abs vec Δw_{vec r} } can be a little bit encumbersome for a game engine. An approximative possibly good-enough alternative could be alignl c_Δt ~sim~ {alignc 1 / {abs vec r}^2 } "."